## Slide 1: Great Cow BASIC Part 7
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 2: PIC16F171xx
PIC16F171xx is a high performance PIC16
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  OpAmp
The PIC16F171xx offers 8 to 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LED
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for Microchip PIC &AVR and Logic Green AVR microcontrollers
Great Cow BASIC now supports the 16F171xx chip family

## Slide 5: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf
By Chris Roper

## Slide 6: Hardware
Layout
By Chris Roper
16F17126

## Slide 7: Pulling it all together
Outputs
  LEDs rotating in sequence
Input
  Switch to control direction of sequence
  Using Master Clear as an input NOT as a reset
ADC
  Read the voltage from the potentiometer
Time
  Using WAIT that consistent across all mcu frequency

## Slide 8: Tutorial overview
Initialise
Flash an LED
Initialise
Do forever
  Read ADC – an 8-bit read
  Determine if switch state changed
  Set state of LEDs
  Wait
Loop
Wait
Set State of LEDS
Left
Right
Do Forever
Set State of LEDs
Switch state changed
ReadADC

## Slide 9: Lab
Examine the sample code
  Review the results
Change the microcontroller !!
  Portable code
Revert the code

## Slide 10
GCStudio Auto Update
Maintains a consistent tool chain
Options
  Automatic
  Off

## Slide 13: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 14: Great Cow BASIC
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021

## Slide 16: Backup Slides

## Slide 17
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes