## Slide 1: Great Cow BASIC
The PIC16F171xx chip Family
Oct 2022

## Slide 2: PIC16F171xx
PIC16F171xx is a high performance PIC16
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  OpAmp
The PIC16F171xx offers 8 to 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – four LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCStudio tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for Microchip PIC, AVR and LGT microcontrollers
Great Cow BASIC now supports the 16F171xx chip family

## Slide 5: Microcontroller
PIC16F17126
5 connections plus decoupling capacitor

## Slide 6: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf

## Slide 7: Hardware
Layout
By Chris Roper

## Slide 8: Hardware
Layout
The LEDs are connected to I/O pins RC0 through RC3. When one of these I/O pins drive high, the LED turns on. The I/O pins can be configured for input or output- on start-up, the default is input. We want digital outputs, so, these must be configured and then we set the RC0 to 1 (ON!)
By Chris Roper

## Slide 9: Basic setup
Install the GCStudio software
  GCBASIC.COM – download page
  SourceForge download directly
Attach and test the
  PICkit2 Low Pin Count Board
  16F17126
Install your programmer and programmer software
  PICKitPlus, NSProg, PK4, another as required

## Slide 10: Setup Summary
Downloaded and installed GCStudio using the default values
Attached microcontroller to the programmer via a suitable board
Validated communications

## Slide 12: Workshop
View Demos
  Press <F4>, select ‘View Demos’
  Select
    Demos\Vendor_Boards\Great_Cow_Basic_Demo_Board\16F17126_chiprange_demonstrations
Three LED programs
  10: Hello World
  20: Blink
  30: Blink another way

## Slide 13: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCStudio tool chain
Assembly and alternatives assemblers
Summary

## Slide 14
Great Cow BASIC for the PIC16F171xx chip Family
January 2021