## Slide 1: Great Cow BASIC Part 18
Great Cow BASIC for the PIC16F171xx chip Family
  October 2022

## Slide 2: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LED
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 3: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for Microchip PIC &AVR and Logic Green AVR microcontrollers
Great Cow BASIC now supports the 16F171xx chip family
Great Cow BASIC is a cross platform with common code translation

## Slide 4: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf
By Chris Roper

## Slide 5: Great Cow BASIC & MPLAB-X/PIC-AS

## Slide 6: The core compiler
Great Cow BASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC and AVR
Reports:
TXT and HTML
Great Cow BASIC Compiler

## Slide 7: Using MPLAB-X
Great Cow BASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
file
Absolute Machine Code
HEX file
8 bit PIC and AVR
PIC-AS,
MPLAB-IDE
Reports:
TXT and HTML
Great Cow BASIC Compiler

## Slide 8: Lab
We will
Review a simple LED program
Create a Project in MPLAB-X using the Great Cow BASIC .S source
  Select Standalone project
  Specify chip, select the Simulator
  Select PIC-AS, latest version
  Name project {chipname}, specify same directory.
  Finish
Now Add the Great Cow BASIC .S source file
    Add existing to “Source Files” using the context menu
    item/select source .S file with AUTO
Select the Project Properties
    Set Conf:[default] Instruction Frequency to 64
    Set Conf:[default] Building – check Execute this line after build to program chip
      ..\PICKitPlus\pickitcommandline.exe -w -p${Device} -f${ImagePath} -mpec -zv -a5
    Press OK to save
Test compile <F11> and program
Use the debugger to walk the code

## Slide 10: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 11: Great Cow BASIC Part 18
Great Cow BASIC for the PIC16F171xx chip Family
  October 2022