## Slide 1: Great Cow BASIC
ASM three ways
Feb 2021

## Slide 2: Overview
Great Cow BASIC supports ASM
  Great Cow BASIC generates ASM for PIC, AVR & LGT
You can use ASM directly in your program
  Compiler will pre-process basic instructions
  Compiler will assemble complex instructions
  Compiler will pass instructions direct to assembler

## Slide 3: The core compiler
Great Cow BASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC and AVR
Reports:
TXT and HTML
Great Cow BASIC Compiler

## Slide 4: 1. Pre-process basic instructions
Just include instructions etc in source
;Display = 8
MOVLW 8
MOVWF DISPLAY,ACCESS
Basic instructions work easily
  Leverage Great Cow BASIC memory management

## Slide 5: 2. Assemble complex instructions
Include instructions etc in source
  Lead with `ASM`
;CLRF TRISC
CLRF TRISC,ACCESS
;MOVLW 0x08
MOVLW 8
;ASM MOVWF Display,ACCESS
MOVWF DISPLAY,ACCESS
Instruction need to use ACCESS and BANKED
Variables need to initialized

## Slide 6: 3. Pass instructions direct to assembler
#ASMRAW CLRF TRISC
#ASMRAW MOVLW 0x08
#ASMRAW MOVWF Display
Include instructions etc in source
  Lead with `#ASMRAW `
Instruction need to handle all syntax
Variables need to defined using #define

## Slide 7: Compare ASM methods
Method | Up’s | Down’s
Just use Great Cow BASIC syntax | Very Portable code Optimised code for chip and config Self documenting Simple | Uses more PROGMEM than asm instructions
Just insert instructions | Leverages Great Cow BASIC memory management and logic control Self documenting | Uses less PROGMEM Chip family specific solution Timing, timers need to be managed
ASM Instruction | Permits range of ASM instructions with some Great Cow BASIC logic control (labels etc) | Uses less PROGMEM Chip family specific solution Timing, timers need to be managed Does not support Great Cow BASIC memory management
#ASMRAW | Permits full range of ASM instructions | # All of above plus any ASM instruction will assembled blindly

## Slide 8: Lab
Method | 
Just use Great Cow BASIC syntax | Baseline creates portable ASM source Baseline with 197 ms delay
ASM Instruction | CLRF TRISC MOVLW 0x08 ASM MOVWF Display,ACCESS
#ASMRAW | #ASMRAW CLRF TRISC #ASMRAW MOVLW 0x08 #ASMRAW MOVWF Display

## Slide 10: Great Cow BASIC

## Slide 11: Great Cow BASIC
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021