## Slide 1: Great Cow BASIC Part 10
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 2: PIC16F171xx
PIC16F171xx is a high performance PIC16
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  OpAmp
The PIC16F171xx offers 8 to 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LED
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for Microchip PIC &AVR and Logic Green AVR microcontrollers
Great Cow BASIC now supports the 16F171xx chip family

## Slide 5: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf
By Chris Roper

## Slide 6: Hardware
http://www.gabotronics.com/development-boards/xmega-xminilab.htm
16F17126

## Slide 7: Pulse Width Modulation
Pulse Width Modulation ( PWM ) is simply a succession of pulses – is a method of reducing the average power delivered by an electrical signal, by effectively chopping it up into discrete parts.
The average value of voltage (and current) fed to the load is controlled by turning on and off at a fast rate. The longer the signal is on compared to the off periods, the higher the total power supplied to the load.

## Slide 8
Goal
Fixed frequency for the period and vary the duty cycle

## Slide 9: CCP/PWM

## Slide 10: Lab
Examine the sample code
  Setup CCP/PWM with PPS
  Read the ADC to set the Duty value
Review the results

## Slide 12: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 13: Great Cow BASIC Part 10
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 14: Backup Slides

## Slide 15: CCP/PWM