## Slide 1: Great Cow BASIC Part 2
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2021

## Slide 2: PIC16F171xx
PIC16F171xx is a high performance PIC16
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  OpAmp
The PIC16F171xx offers 8 to 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for Microchip PIC, AVR and LGT microcontrollers
Great Cow BASIC now supports the 16F171xx chip family

## Slide 5: Microcontroller connectivity
PIC16F17126

## Slide 7: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf

## Slide 8: Hardware
Layout
By Chris Roper

## Slide 9: Basic setup - recap
Downloaded and installed GCStudio using the default values
Attached microcontroller to the programmer via a suitable board
Validated programming communications

## Slide 10: Lab Cam

## Slide 11: Make four LEDs flash in a sequence
Initialise
Set 1st LED
Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes

## Slide 12: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 13: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 14: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 15: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 16: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 17: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 18: Rotate with Carry
 | LED4 = C.3 | LED3 = C.2 | LED2 = C.1 | LED1 = C.0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 19: Workshop

## Slide 20: Great Cow BASIC
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 21: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary