## Slide 1: Great Cow BASIC Part 5
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 2: PIC16F17126
PIC16F171xx is a high performance PIC16
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  OpAmp
The PIC16F171xx offers 8 to 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LED
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for Microchip PIC &AVR and Logic Green LGT8F328P microcontrollers
Great Cow BASIC now supports the 16F171xx chip family

## Slide 5: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf
By Chris Roper

## Slide 6: Hardware
Layout
By Chris Roper

## Slide 7: Switch
The switch is connected RA3
When the switch is depressed RA3 will transition to 0v

## Slide 8: Tutorial overview
Initialise
Set LED off
Keypressed = TRUE
Initialise
Check the switch
  If pushed then toggle LED
  If not pushed then do it again
Checking the switch call a method to inspect the state
Loop
Toggle LEDs
No
Yes

## Slide 9: Lab
Examine the sample code
Review the results
Change from PICKit2 to
  PICKit3 programmer
  PICKit4 programmer

## Slide 11: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 12: Great Cow BASIC
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 13: Backup Slides

## Slide 14
Initialise
Set LED off
Keypressed = TRUE
Loop
Toggle LEDs
No
Yes