## Slide 1: Great Cow BASIC Part 4
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 2: PIC16F17126
PIC16F171xx is a high performance PIC16
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  OpAmp
The PIC16F171xx offers 8 to 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for PIC and AVR microcontrollers
Great Cow BASIC now supports the 16F171xx chip family

## Slide 5: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf
By Chris Roper

## Slide 6: Overview
Great Cow BASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  Great Cow BASIC makes the process easy via the ReadADC12() - a value of 0 to 4095
Wait for a time period based on ADC
Set the LEDs
Do it again….and, again

## Slide 7: Time
This tutorial combines previous tutorials by using WAIT() to control the speed of LED rotation based on the ADC value.
  Where speed is a time delay
    us, 10us, ms, 10ms, s, m or h
    wait time unit - wait 1 ms
  Where the code, by Great Cow BASIC, generated is a function of the frequency of the microcontroller automatically

## Slide 8: Flow
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Time delays are sometimes key to the operation of a program
Read ADC 12 bit
( 0 – 4095 )

## Slide 9: Lab
Examine the sample code
Review the results

## Slide 11: Scale
Scale()
Scale transforms an existing value to a new value within a specified scale
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Read ADC

## Slide 12: Lab
Revise the sample code
Review the results

## Slide 14: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 15: Great Cow BASIC
Great Cow BASIC for the PIC16F171xx chip Family
Oct 2022

## Slide 16: Backup Slides

## Slide 17
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes

## Slide 18: Analog-to-Digital